## Slide 1: Predicting Wind Turbine Failures Before They Happen A Cost-Optimised Classification Approach ReneWind Austin University – Post Graduate Program in Artificial Intelligence 2026-03-14

## Slide 2: Contents / Agenda
Executive Summary
Business Problem Overview and Solution Approach
Data Overview
EDA Results
Data Preprocessing
Model Evaluation Criterion
Model Performance Summary
Test Performance of Best Model
Appendix

## Slide 3: Executive Summary
Business Recommendation
Deploy Model 5
Bundle StandardScale with the Model
Monitor sensors V18, V21, V15, v7

## Slide 4: Executive Summary
Business Interpretation of the Results
248 Failures caught (True Positives)
Turbines flagged before failure and repaired on schedule. Repair cost incurred – significantly lower than replacement. This is the optimal outcome
~34 missed failures(False Negatives) -- primary risk
Turbines that will fail without a maintenance flag. Full replacement cost incurred. These are the primary remaining business risk and the target for future model improvement via SMOTE. In preliminary tests it achieved better rates.
~8 false alarms (False Positives) Healthy turbines flagged for inspection. Tech dispatched, no fault found. Inspection cost only – The lowest cost outcome. At only 8 false alarms on 5,000 predictions, this is exceptionally low and operationally manageable
TP = 0.88 × 282 = 248.16 → ~248 failures correctly caught
FN = 282 - 248 = 34 → ~34 failures missed
Precision = TP / (TP + FP)
0.97 = 248 / (248 + FP)
248 + FP = 248 / 0.97
248 + FP = 255.67
FP = 255.67 - 248
FP ≈ 7.6 → ~8

## Slide 5: Business Problem Overview and Solution Approach
Problem Definition
  ReneWind collects data from 40 sensors fitted across wind turbine generators to predict mechanical failure before it occurs. ReneWind needs to find the best way to implement predictive maintenance for turbine generators based on the high-density sensor network data provided
  Sensor Array:
  40 telemetry features (V1 - V40) monitoring turbine health.
  Dataset Scale:
  25,000 total observations (20k Train / 5k Test).
  The "Needle in the Haystack" Challenge:
  Class Imbalance:
      17:1 ratio of Normal operation to Failure.
  Minority Class:
Only 5.55% of the data represents actual failure events.

## Slide 6: Business Problem Overview and Solution Approach
Cost-Benefit Approach
In wind energy, not all errors are equal. Our model logic is dictated by the cost of being wrong.
The cost structure is asymmetric. A missed failure leads to unplanned breakdown and full generator replacement — the most expensive outcome. A correct prediction enables a scheduled repair at moderate cost. A false alarm triggers only a cheap inspection.
This hierarchy makes Recall the primary metric — catching failures matters more than avoiding false alarms.
Scenario | Event | Outcome | Cost Impact
False Negative | Missed Failure | Unplanned Breakdown | 🔴 Critical (Full Replacement)
True Positive | Correct Prediction | Scheduled Repair | 🟡 Moderate (Maintenance)
False Positive | False Alarm | Unnecessary Inspection | 🟢 Low (Technician Visit)

## Slide 7: Business Problem Overview and Solution Approach
Please mention the solution approach/methodology
  The objective is to build various classification models, tune them, and select the best one to identify failures, so the generators can be repaired before failing or breaking, reducing overall maintenance costs. Considering the cost structure is asymmetric and drives every modelling decision, the nature of predictions made by the classification model will translate as follows:
  Missed failure (False Negative)
    Results in unplanned generator breakdown and full replacement — the highest cost outcome
  Correct prediction (True Positive)
    Triggers a scheduled repair — moderate cost, significantly cheaper than replacement
  False alarm (False Positive)
    Rriggers an unnecessary inspection — the lowest cost outcome

## Slide 8: EDA Results
The training dataset
  Dataset Dimensions:
    20,000 training records | 5,000 test records.
  Feature Profile:
    40 numerical sensor inputs (float64) and 1 binary integer target.
  Class Definition:
    0 (Normal Operation) vs. 1 (Equipment Failure).
  Data Integrity:
    38 of 40 features were 100% complete.
  Missing Value Strategy:
    Features V1 and V2 contained missing values(approx 0.09). These were resolved via Median Imputation to maintain the integrity of the feature distributions while being robust to potential outliers.
  Metadata Quality:
    For security reasons, the feature names were scrambled, creating meaningless names. It diffuses the quality of the analysis due to a lack of better context
Link to Appendix slide on data background check

## Slide 9: Data Preprocessing
Duplicate value check
  No Duplicate value found in Train and Test.
Missing value treatment
  The training data features V1 and V2 contained missing values(approximately 0.09). These were resolved via Median Imputation to maintain the integrity of the feature distributions while being robust to potential outliers. We applied the same procedure to missing V1 and V2 features in the test data.

## Slide 10: Data Preprocessing
Outlier check (treatment if needed)
  The outlier rates are low but not zero. V34 is the highest in the dataset.
  The spikes are important; we kept the outliers because these are the way
  for the turbine to notify that it is about to break. V18 and V15 are in the top 5
  Predictors. They are the most correlated with failure. If we removed then
  we would get rid of the most informative signal in the dataset.
  Relu also handles outliers well, another reason to keep them.
Feature | Outlier %
V34 | 4.02%
V18 | 3.66%
V15 | 2.57%
V33 | 1.92%
V29 | 1.68%
V35 | 1.58%
V24 | 1.54%
V13 | 1.52%
V17 | 1.48%
V7 | 1.46%

## Slide 11: Data Preprocessing
Feature engineering
  Two transformations were applied to V1 and V2 using median imputation. It replaced the 18 values in the training dataset and 5 and 6 values in the test dataset.
  StandardScaler normalization transformed all 40 features, changing their basic scale. It helped with gradient descent. This was not in the low-code notebook. I applied it to enhance Recall using SMOTE, which I will briefly comment on at the end.
  Feature engineering was intentionally minimal.
  We considered applying dimensionality reduction because of the 40 features. It was not applied because NN handles these features well.
  Feature vs Feature correlation is <0.3, mostly low. There is low redundancy and high density.
  Feature vs Target correlation is small; It requires a deep learning model to find patterns

## Slide 12: Data Preprocessing
Data preparation for modeling
  The target variable is severely imbalanced — 18,890 observations (94.45%) belong to class 0, and only 1,110 (5.55%) to class 1, resulting in a 17:1 ratio.
  Balance class weights were computed using sklearn compute_class_weight at the rate [0.52, 9.009] to invert the imbalance contribution mentioned above.

## Slide 13: Model Evaluation Criterion
Because a missed failure costs significantly more than a false alarm, we cannot rely on standard "Accuracy." We use a specific set of tools to measure performance.
Primary metric Recall
To measure the proportion of actual failures correctly identified by the model. It is the primary business metric because the cost of a turbine is much higher than maintenance costs. Recall = TP / (TP + FN).
At threshold 0.3: 248 of 282 failures caught → Recall = 0.88
Secondary metric Precision
To measure the proportion of alerts that are genuine failures. It cannot be ignored, as it can cause up to 4718 unnecessary maintenance trips. At that point, the overall cost may surpass the cost of a turbine.
Precision = TP / (TP + FP)
At threshold 0.3: only ~8 false alarms out of ~256 alerts → Precision = 0.97

## Slide 14: Model Evaluation Criterion
Because a missed failure costs significantly more than a false alarm, we cannot rely on standard "Accuracy." We use a specific set of tools to measure performance.
Support metric F1
IT is the harmonic mean of precision and recall. F1 penalizes extreme imbalance between the two. It was not used as a primary metric because it assumes equal cost for false positives and false negatives. For ReneWind false negative is extremely costly for it would mean to replace a turbine.
Reference metric Accuracy
It was not used for model selection due to class imbalance.
Threshold Tuning
Used to maximize Recall, given we want to consider even the borderline fail possibility. The default threshold of 0.5 was reduced to 0.3 across all final evaluations. This adjustment reflects the cost asymmetry directly — at 0.3, the model acts on lower-confidence failure signals, catching borderline cases that would otherwise be missed. The table below shows the effect of the threshold on the key metrics:
Threshold Recall Precision F1 False alarms Missed failures
0.5 0.86 0.96 0.91 ~10 ~39
0.3 0.88 0.97 0.92 ~8 ~34

## Slide 15: Model Evaluation Criterion
Metric | Role | Formula | Final value
Recall | Primary — minimise missed failures | TP / (TP + FN) | 0.88
Precision | Constraint — limit false alarms | TP / (TP + FP) | 0.97
F1 score | Balance check | 2×P×R / (P+R) | 0.92
Accuracy | Reference only — not used for selection | (TP+TN) / Total | 0.98
Best Model on Test Results

## Slide 16: Model Performance Summary
The average time to run was 30s, with SGD models slightly faster than ADAM at 26s.
Model 5 is the best all-around performance. It leads to Accuracy, Precision, and F1. With Recall At 0.9365, it is just below the top 2. The combination makes it the most reliable model.
Model 6 leads in recall but has the lowest precision of all; it generates more false alarms.
Model 3 offers an interesting middle ground; it is more aggressive for failure detection with slightly more false alarms.
Link to Appendix slide on model assumptions
 | Model 0 | Model 1 | Model 2 | Model 3 | Model 4 | Model 5 | Model 6
Accuracy | 0.989250 | 0.990750 | 0.989500 | 0.989000 | 0.991000 | 0.992250 | 0.988250
Recall | 0.909513 | 0.929386 | 0.924485 | 0.943299 | 0.933758 | 0.936540 | 0.945022
Precision | 0.986649 | 0.980696 | 0.972933 | 0.950956 | 0.978684 | 0.988704 | 0.943144
F1 Score | 0.944343 | 0.953407 | 0.947230 | 0.947090 | 0.954971 | 0.960963 | 0.944080

## Slide 17: Best Model - Test Performance
Architecture of the best model
Comments on the best performance model on the test set
It was evaluated on the held-out test set of 5,000 observations at a classification threshold of 0.3, which was chosen to capture all possible
The model performed well, capturing 88% of failures, achieving 97% real alert rate, and achieving the best-balanced F1 score of 0.92. It achieved approximately 8 false alarms out of 5000 predictions.
Link to Appendix slide on model assumptions
INPUT
40
Sensor features
HIDDEN LAYER 1
128
ReLU
REGULARIZATION
0.5
dropout
HIDDEN LAYER 2
64
ReLU
HIDDEN LAYER 3
32
ReLU
OUTPUT
1
Sigmoid
Metric | Class 0 (No failure) | Class 1 (Failure) | Macro avg
Precision | 0.99 | 0.97 | 0.98
Recall | 1.00 | 0.88 | 0.94
F1 score | 1.00 | 0.92 | 0.96
Support | 4,718 | 282 | 5,000

## Slide 18: APPENDIX

## Slide 19: Slide Header
Please add any other pointers (if needed)